## Slide 1
Study on the “Potential of a full EV-power-system-integration in Europe & how to realise it”
Study Results - October 27th 2024
Marian Klobasa, Annegret Stephan, Benjamin Lux, Fabio Frank – Fraunhofer Institute for Systems and Innovation Research ISI, Karlsruhe
Janis Kähler, Arne Surmann, Wolfgang Biener, Matthias Kühnbach, - Fraunhofer Institute for Solar Energy Systems ISE, Freiburg

## Slide 2: Study Results
Key topics and research questions
      Power System Perspective: Costs and savings from EV charging as a flexibility resource (Marian Klobasa, Fraunhofer Institute for Systems and Innovation Resrearch ISI)
        What is the benefit of bidirectional charging in the EU power market and in its Member States?
        How does bidirectional charging enable the system integration of renewable energy sources?
      Grid Perspective: Costs and savings from vehicle to grid (Janis Kähler, Fraunhofer Institute for Solar Energy Systems ISE)
        What are the costs and savings generated through a large-scale application of bidirectional charging, particularly with regard to the electrical grid system?
      User perspective: Cost-benefit analysis of smart and bidirectional charging at home (Janis Kähler, Fraunhofer Institute for Solar Energy Systems ISE)
        What are the potential gains for EV users when applying smart unidirectional or bidirectional charging at home?
      Conclusions on key benefits from smart and bidirectional charging
      Not part of the webinar today:
      Promise of V2X: Drivers and Barriers
      Country specific results for Germany, France, Spain, Italy, Poland and UK (

## Slide 3
Power System Perspective

## Slide 4: Modelling approach and scenario set up
Enertile and Aladin system models
    Assessment of absolute/relative changes in annual system costs for different scenarios.
      fixed annual costs
        generation of electricity, heat and hydrogen
        annualized investment along with fixed operating and maintenance costs (fixed O&M)
      variable annual costs
        hourly operation generating electricity and heat
        fuel costs, CO2 costs and variable operating and maintenance costs (variable O&M)
      financing costs for electricity and hydrogen transport infrastructure and storage.
      no additional costs are assumed for bidirectional charging compared to uncontrolled charging.
Source: Lux 2022

## Slide 5: Input data and assumptions
Scenarios and number of EVs, trucks and vans
Scenario variants based on TransHyDe project – S2 scenario | 
Reference - Uncontrolled: | Uncontrolled charging of all cars and trucks, vans Deterministic e-mobility load
Cars Controlled V2G: | Specific share of cars can participate in smart and bi-directional charging Cars are full-fleged system storages.
Cars and Trucks, Vans Controlled V2G: | Specific share of cars and trucks can participate in smart and bi-directional charging Cars are full-fleged system storages.
Source: Lux 2022

## Slide 6: Energy and electricity demand in transport 2030 and 2050
Development of final energy demand and availability of EVs for V2G

## Slide 7: Changing Power Systems with V2G
EU power system
Electricity generation
Installed capacities
Portfolio shift of renewables from wind/CSP to PV capacity
Decrease of flexibil generation and storage capacities
  Decrease of hydrogen power plants as back up capacities
  Decrease of stationary battery storage
Shift in renewable generation from wind/CSP to PV generation
Utilization of cars for V2G discharge

## Slide 8: Results on cost savings
EU power system benefits from smart and bidirectional charging
Cost savings of 22.2 billion EUR in 2040
Smart charging and bidirectional charging reduces system costs by 8.6 % in 2040
        Less peak capacity during hours of high residual loads
        Better integration of PV generation.
Investment needs for alternative storage technologies and back-up power plants reduced

## Slide 9
Grid Perspective

## Slide 10: Methodology
 | 2030 | 2040
Mio. HP | 4.3 | 10
Mio. EV | 14.1 | 30.7
PV rooftop in GW | 129 | 240
Grid System Perspective
Grids

## Slide 11: Grid System Perspective
Effect of grid different control strategies of Grid expansion costs in Germany
Grouped by urbanization types and calculated for uncontrolled charging economically optimized charging and grid friendly controlled charging
Grid friendly: Assuming a monitoring of the transformer loading by DSOs and requesting bi-directional flexibility from plugged-in EVs
EUR10.75 billion for 2030 with higher cost for low densities for the uncontrolled case of EVs. Only a slight reduction by the controllers
In 2040 the costs rise to EUR29 billion in the uncontrolled case. The grid friendly controlled EVs can slightly reduce the costs in all regions to a total of EUR27.27 billion

## Slide 12: Grid System Perspective
Interpolate the results to other European Countries
Based on the distribution of the population by country to the three urbanization types the results are interpolated
Potential savings in grid expansion costs when applying grid friendly controlled charging for 2040: EUR10.6 billion for EU28
densely
populated
medium
density
sparsely populated
sum
2040

## Slide 13
User Perspective

## Slide 14: User Perspective
Methodology

## Slide 15: User Perspective
Methodology
Different control strategies
Notes: Baseline: Upon arrival, the EV is charged with maximum power until the target SOC is reached.
PV optimized:
  Unidirectional: The EV is charged preferably with the PV power available. If the energy provided by the PV plant is not sufficient to guarantee the target SOC, the remaining energy is charged from the grid.
  Bidirectional: The EV is charged with as much PV power as possible whenever available and is discharged to supply household appliances when possible while still guaranteeing the target SOC upon departure with the highest possible solar energy mix within the battery.
Price optimized:
  Unidirectional: The EV is charged when household electricity prices are lowest.
  Bidirectional: The EV is used to charge electricity during low price periods to supply it later to the household appliances if the price spread is high enough to compensate for the charging/discharging losses. Otherwise, the EV is charged within the low-price windows to meet target SOC. Note that no trading back to the market is considered.
PV and Price optimized (uni- & bidirectional): A mixture of PV and Price optimized where PV is considered to have zero costs.

## Slide 16: User Perspective
Methodology
Different control strategies

## Slide 17: User Perspective
Methodology
Different control strategies
Notes: Baseline: Upon arrival, the EV is charged with maximum power until the target SOC is reached.
PV optimized:
  Unidirectional: The EV is charged preferably with the PV power available. If the energy provided by the PV plant is not sufficient to guarantee the target SOC, the remaining energy is charged from the grid.
  Bidirectional: The EV is charged with as much PV power as possible whenever available and is discharged to supply household appliances when possible while still guaranteeing the target SOC upon departure with the highest possible solar energy mix within the battery.
Price optimized:
  Unidirectional: The EV is charged when household electricity prices are lowest.
  Bidirectional: The EV is used to charge electricity during low price periods to supply it later to the household appliances if the price spread is high enough to compensate for the charging/discharging losses. Otherwise, the EV is charged within the low-price windows to meet target SOC. Note that no trading back to the market is considered.
PV and Price optimized (uni- & bidirectional): A mixture of PV and Price optimized where PV is considered to have zero costs.

## Slide 18: User Perspective
Methodology
Different control strategies
Notes: Baseline: Upon arrival, the EV is charged with maximum power until the target SOC is reached.
PV optimized:
  Unidirectional: The EV is charged preferably with the PV power available. If the energy provided by the PV plant is not sufficient to guarantee the target SOC, the remaining energy is charged from the grid.
  Bidirectional: The EV is charged with as much PV power as possible whenever available and is discharged to supply household appliances when possible while still guaranteeing the target SOC upon departure with the highest possible solar energy mix within the battery.
Price optimized:
  Unidirectional: The EV is charged when household electricity prices are lowest.
  Bidirectional: The EV is used to charge electricity during low price periods to supply it later to the household appliances if the price spread is high enough to compensate for the charging/discharging losses. Otherwise, the EV is charged within the low-price windows to meet target SOC. Note that no trading back to the market is considered.
PV and Price optimized (uni- & bidirectional): A mixture of PV and Price optimized where PV is considered to have zero costs.

## Slide 19: User Perspective
Cost reduction of bidirectional charging
The simulation results show large cost saving potentials for controlled charging
The plot shows the total electricity bill for a teleworker for baseline scenarios in different countries compared to bidirectional control strategies
For unidirectional charging two German fulltime workers can reduce costs by 21 %, a family by 22 % and a teleworker by 36 % when following a combined control approach for PV- and price optimization
Similar findings are true for the other observed countries with different absolute values in cost savings.
unidirectional charging

## Slide 20: User Perspective
Cost reduction of bidirectional charging
The simulation results show large cost saving potentials for controlled charging
The plot shows the total electricity bill for a teleworker for baseline scenarios in different countries compared to bidirectional control strategies
For unidirectional charging two German fulltime workers can reduce costs by 21 %, a family by 22 % and a teleworker by 36 % when following a combined control approach for PV- and price optimization
Similar findings are true for the other observed countries with different absolute values in cost savings.
Applying bidirectional charging, the costs saving can be further increased by up to 9 %. This additional potential from bidirectional energy is subject to additional losses for charging-discharging cycles with low part load efficiencies and the major PV excess already being exploited during the EV charging.
bidirectional charging

## Slide 21
Conclusion

## Slide 22: Conclusions
Benefits beyond gains for individual EV users
      Smart charging and V2G is beneficial to relief transformation pressure in all of the mentioned areas
        Decrease in curtailment and in electricity imports
        Better integration of PV capacity, more capacity can be installed
        Reduced need for alternative flexibility resources in the system
          Less stationary battery storage
          Reduced electrolysis and reduced electrification of H2/Natural Gas
      Benefits of V2G compared to smart charging
        Decrease of back-up capacities of gas and hydrogen power plants
        Lower utilization of power generation from gas and hydrogen power plants
      Truck flexibility: Marginal additional value of truck flexibility if passenger cars are already bidirectional
        More effective integration of PV through passenger cars, if cars are connected at day-time
        Market can be saturated even without use of truck flexibility
      => Additionally individual benefits for EV users occur and increase with higher price variability and market participation

## Slide 23
Contact
    Dr. Marian Klobasa
    Geschäftsfeld Energiemanagement
    und Intelligente Netze
    Tel. +49 721 6809 -287
    marian.klobasa@isi.fraunhofer.de
      Fraunhofer-Institut für System- und Innovationsforschung ISI
      Breslauer Straße 48, 76139 Karlsruhe
      www.isi.fraunhofer.de